## Slide 1
İşletmelerde Toz Tehlike Analizleri (TTA) ve Risk Azaltıcı Önlemler
Emre Ergun, IEP Technologies Türkiye GM
emre.ergun@hoerbiger.com, M: 0533-457-4412
18/05/2022

## Slide 2: IEP Technologies Hakkında
IEP Türkiye Ofisi Kuruluşu, 2015 sonu

## Slide 3: IEP Technologies Hakkında
IEP Technologies Türkiye: Merkez İzmir, Depo İstanbul
  Türkiye’de ofisi olan tek patlama korunma sistemi üreticisi
  Patlama korunma ve engelleme sistemleri sistem tasarımları
  Sistem seçimleri ve ihtiyaç analizleri
  Kurulumlarda sistem kontrolleri ve devreye alım
  Periyodik sistem bakımları, acil müdehale, olay sonrası analizler
  Patlama Korunma ve Engelleme Sistemleri Eğitimleri
  IEP Technologies Global garantisi altında hizmet

## Slide 4: Toz Patlar mı ? Bizde toz patlaması olmaz... Bizim malzememiz patlayıcı değil ... Bizim ekipmanda yüksek basınç yok... Bizde bugüne kadar hiçbir olay yaşanmadı...

## Slide 5: Bizde Patlama Olmaz – Yem/Tahıl
Ref - Journal of Loss Prevention in the Process Industries 62 (2019) 103928

## Slide 6: Bizde Patlama Olmaz- Yem/Tahıl
Alevlenme değirmende başlar
Değirmen filtresi içinde toz patlaması yaratır (ZONE20 ortam)
Patlama bağlantılı boru hatlarından diğer ekipmanlara yayılır
Ekipmanlarda oluşan hasarla, bina içine üretim alanlarına dağılır (ZONE22)
İkincil patlamalar bina içinde devam eder...
Ta ki yakıt bitene kadar...

## Slide 7: Bizde toz patlaması olmaz.../Ahşap

## Slide 8: Bizde toz patlaması olmaz.../Kağıt
Filtre de patlama ve devamında yangın...
Ref- ABD Kağıt Fabrikası Yangın ve Patlaması

## Slide 9: Bizde toz patlaması olmaz.../Kağıt

## Slide 10: Bizde Patlama Olmas.../Geri Dönüşüm

## Slide 11: Kovalı Elevatör Patlaması

## Slide 12: Tahıl Deposu Patlaması

## Slide 13: Şeker FabrikasıPatlaması

## Slide 14: Metal - Jant Fabrikası Metal Tozu Patlaması

## Slide 15: Boya Sektörü – Filtre Patlaması

## Slide 16: Gıda– Süt Tozu Üretimi Kurutma Sistemi Patlaması

## Slide 17: Toz Tehlike Analizleri
Kapsam- fabrikanın hangi bölgeleri ?
TTA Takımı oluşturulması
Proses bilgileri ve işlenen Toz Malzemelerin Alevlenme Özelliklerinin belirlenmesi !!!!
Saha ziyareti ve incelemeler
İncelenen ekipmanlar ve ortamlarda toz parçacık dağılımları belirlenmesi
Ortamda toz birikimleri incelenmesi
EX ZONE kontrolleri (ekipmanlar, çalışma alanları)
Alev kaynakları analizi EN1127-1, alevlenme olasılığı belirlenmesi
Ekipmanlar arası bağlantıların incelenmesi – olası patlama/yangın yayılımları
Geçmiş kaza ve ramak kalaların incelenmesi
Şu anda kullanılan risk kontrolleri ve yeterlilikleri (NFPA68, 69, 654, VDI, BSI)
GAP Analizi
  Kalan riskin yüksek olduğu bölge/ekipmanların belirlenmesi
  Yeni/ek patlama korunma/engelleme sistemleri seçilmesi, hesaplanması
  Öneriler ve uygulama
Tekrar. Periyodik olarak raporların incelenmesi ve olası proses/malzeme değişimlerinin risklere etkisinin belirlendikten sonra güncellemelerin yapılması
Ref – NFPA652
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 18: Toz Patlamaları – Nasıl Oluşur?
Toz veya gaz halindeki yakıtın kıvılcım ile alevlenmesi ve hızlıca yanması ile başlar
Ani ve yüksek miktarda gaz açığa çıkar (yanma tepkimesi)
İç basıncın artışından kaynaklanarak parçalanan konteynerden çıkan ani gaz ve alev topu patlama olarak adlandırılır

## Slide 19: PATLAMA RİSKİ TAHMİNİ
Risk = Pzon * CPign * DPmax
R: Patlama riski
P : Tehlikeli durum faktörü (hazard factor), patlayıcı ortam oluşma olasılığı (EX ZONE)
C : tehlikeli durumun zarar oluşturma olasılığı: EN1127-1
(ALEV KAYNAĞI BULUNMA OLASILIĞI VE SÜRESİ)
D : zarar faktörü, zararın büyüklüğünün tahmini
(PATLAMA ŞİDDETİ, Kst, Kg gibi değerler)
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 20: Riskli Endüstriler ve Maddeler
REF – USA OSHA

## Slide 21: Riskli Endüstriler ve Maddeler

## Slide 22: Riskli Ekipmanlar
Bölgeler | ABD (1985 – 1995) |  | İngiltere (1979 – 1988) |  | Almanya (1965 – 1980) | 
 | Olay Sayısı | % | Olay Sayısı | % | Olay Sayısı | %
Toz Toplayıcılar | 156 | 42 | 55 | 18 | 73 | 17
Değirmenler | 35 | 9 | 51 | 17 | 56 | 13
Taşıma sistemleri | 32 | 9 | 33 | 11 | 43 | 10
Silo/Bunkerler | 27 | 7 | 19 | 6 | 86 | 13
Kurutma / Kazan Sistemleri | 22 | 6 | 43 | 14 | 34 | 8
Karıştırıcılar | >12 | >3 | 7 | 2 | 20 | 5
Diğerleri / Bilinmiyor | 84 | 23 | 95 | 31 | 114 | 27
Toplam | 372 | 100 | 303 | 100 | 426 | 100
REF: Guidelines for Safe Handling of Powders and Bulk Solids, CCPS, AICHE

## Slide 23: Sigorta İstatistikleri- Ekipman Hasarları
REF- FM Global 1983-2006

## Slide 24: İkincil Patlamalar: Kontrolsüz Risk
İkincil patlamalar, ana patlamanın alev ve basıncının bağlantılı ekipmanlara ve ortama yayılması ile oluşur (borular, şutlar, konveyörler, …vs )
Yetersiz fabrika temizliği
Ortamda toz birikimi ~1mm +
Ref – US Chemical Safety Board,

## Slide 25: Ortama Toz Kaçakları
Aşırı miktarda havada askıda yanıcı toz !!!

## Slide 26: Ortamda Toz Birilimi: İkincil Patlamalar

## Slide 27: Ortamda Toz Birilimi: İkincil Patlamalar
Enerji Santrali Kömür değirmeni alanı:
Yerde 5-15cm arası toz birikimi (sınır 3mm!!!)
Değirmende olası bir patlamanın sonuçları ?

## Slide 28: Ortamda Toz Birilimi: İkincil Patlamalar

## Slide 29: Tehlikeli Bölge / ZONE Sınıfları (TOZ)
Biriken Tozun Derinliği (mm) | Birikim Sıklığı | Temizlik Prosedürü | Tehlikeli Alan Sınıfı (Zone)
Yüzey renginde değişiklik belirli değil | Yok | Yok | Sınıflandırma dışı (genel amaçlı alan)
<0.8 | Az sıklıkta. < Senede 3 defa | Oluştuğu vardiya sırasında | Sınıflandırma dışı (genel amaçlı alan)
<0.8 | Devamlı veya sık > senede 3 defa ve toz birikim 24 saat içinde | Avaraj toz birikimi 0.4mm nin altında kalacak şekilde düzenli temizlik | Sınıflandırma dışı ancak dust-tight(IP 6x, NEMA 4)
0.8 - 3mm | Az sıklıkta. < Senede 3 defa | Oluştuğu vardiya sırasında | Sınıflandırma dışı ancak toz-korunaklı kutu (IP 6x, NEMA 4)
0.8 - 3mm | Devamlı veya sık > senede 3 defa ve toz birikim 24 saat içinde | Avaraj toz birikimi 1.5 mm nin altında kalacak şekilde düzenli temizlik | Class II Div 2, ZONE 22
>3 mm | Az sıklıkta. < Senede 3 defa | Oluştuğu anda sistemi durdurup temizlik yapılması | Class II Div 2, ZONE 22
>3 mm | Devamlı veya sık > senede 3 defa ve toz birikim 24 saat içinde | Düzenli temizlikle toz birikimini minimize et | Class II Div 1, ZONE 21
NFPA 654 Metodu
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 30: Hangi Toz Daha Kolay Alevlenir?
500 Micron Altı Parçacık Büyüklüğü ?
Parçacık büyüklüğü dağılımı ?
Rutubet Oranı ?
Kimyasal bileşenleri? (hibrid durum var mı?)
MIE, AIT ???
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 31: Parçacık Büyüklüğü ve Havada Asılı Kalma Süresi
 | Parçacık büyüklüğü, Mikron
Masa Tuzu | 100
Toz Şeker | 450-600
Kum | 50+
Bebek Pudrası | 10
İnsan saçı | 40-300
Un | 1-100
500 mikron altı parçacık büyüklüğü ‘toz’ sınıfına girer
Yanıcı tozlarda parçacık büyüklüğü azaldıkça patlama riski artar
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 32: Patlayıcı Tozların Özellikleri
Go/No Go
BZ Sınıfı (yanma hızı)
Toz bulutu reaktivitesi(Pmax and Kst), ASTM E1226
Toz bulutunun minimum alevlenme sıcaklığı (AITc), ASTM E1491
Toz tabakası min alevlenme sıcaklığı (AITl), ASTM E2021
Toz bulutunun minimum tutuşma enerjisi (MIE), ASTM E2019
Minimum patlayabilir toz bulutu konstantrasyonu (MEC), ASTM E1515
Minimum oksijen konstantrasyonu (MOC), ASTM E2931
İçten yanma Onset Sıcaklığı (UN Metodu)
MIE Test Ekipmanı
20lt Kuhner (Kst, Pmax, MEC, MOC)
BAM Fırını
AITc Test Ekipmanı
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 33: Patlayıcı Toz St Sınıflandırılması
1 -200 (orta)
ST - 2
ST Sınıfı
K
st
Değeri
ST - 1
201 – 300 (şidetli)
ST - 3
301 and above (çok şidetli)
Madde | Medyan Çap mikron | Kst Bar.m/sec | Pmax Bar | MEC g/m3
Mısır tozu | 28 | 75 | 9 | 60
Odun | 59 | 146 | 8 | 70
Şeker | 41 | 154 | 8 | 60
Toz Boya | 20 |  | 7 | 30
Linyit | 32 | 151 | 10 | 60
REF – NFPA 68, CRC
PATLAMA KORUNMA SİSTEM TASARIMINDA GEREKLİDİR !!!!
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 34: Toz Malzemelerin Patlama Özellikleri
 | Minimum Alevlenme Sıcaklığı, MIT [oC] | Minimum Alevlenme Enerjisi, MIE [mJ] | Alt Patlama Sınırı, MEC [g/m3] | Maksimum Patlama Basıncı, Pmax [bar] | Maksimum basınç artış hızı, Kst [bar.m/s] | ST Sınıfı
KULLANIMI | Güvenli proses sıcaklığı, risk analizi | Risk Analizleri, elektrostatik kontroller | ZONE belirlenmesi | P.K sistem tasarımı, patlama etkisi | P.K. Sistem tasarımı | -
Kömür | 525 | 110 | 60 | 9.2 | 129 | 1
Petkok | 670 | 1000 | 125 | 7.6 | 47 | 1
Linyit | 425 | 160 | 60 | 10 | 151 | 1
Mısır | 400 | 40 | 45 | 6.55 | 137 | 1
Mısır Koçanı | 400 | 40 | 30 | 7.6 | 115 | 1
Mısır Nişastası | 380 | 20 | 40 | 7.9 | 206 | 2
Pamuk Linteri | 520 | 192 | 500 | 3.3 | 3.5 | 1
Tahıl, karışık | 430 | 30 | 55 | 7.9 | 126 | 1
Pirinç | 440 | 40 | 45 | 6.4 | 82 | 1
Şeker | 350 | 30 | 35 | 6.3 | 115 | 1
Buğday | 480 | 60 | 55 | 7.1 | 82 | 1
Ref NFPA 68, 61, 499
UYARI – Yukarıdaki değerler , tozun parçacık büyüklüğü ve rutubet oranına göre değişir

## Slide 35: İçten Yanma – Malzeme Birikimi ve Alevlenme İlişkisi
100degC

## Slide 36: MIE Alevlenme Enerjisi ve Risk Analizi İlişkisi
MIE | Tozları Alevlendirme Olasılığı, Pign
0 < mie < 10mj | 100%
10 < mie < 100mj | 10%
100mj < mie | 1%
Sıcak iş, rulman sürtünmesi, kıvılcım, vs | 100%
ref AICHE CCPS

## Slide 37: Malzeme bilgisi proses risk analizinde nerelerde kullanılır?
Proses / Test | Go/No Go | MIE (mJ) | AIT_toz bulutu, C | AIT_ toz tabakası, C | Kst (bar.m/sec) | MOC (%) | MEC (g/m3) | İçten Yanma (degC) | Volume Resistivity | Chargeability
Malzeme transfer/ boşaltma | X | X |  |  |  |  |  |  | X | X
Eleme | X | X |  |  |  |  |  |  | X | X
Karıştırma (tumble/double cone blending) | X | X |  |  | X | X | X |  | X | X
Ribbon Blending | X | X | X | X |  |  |  |  | X | X
Öğütme (değirmenler) | X | X | X | X | X | X |  | X | X | X
Jet değirmenler | X | X |  |  | X | X |  |  | X | X
Spray/FB/Flash/Döner Kurutucu | X | X | X | X | X |  | X | X | X | X
Bantlı Kurutucular | X | X |  |  |  |  |  | X |  | 
Pünematik Taşıma | X | X |  |  |  |  | X |  | X | X
Helezon/Vidalı Taşıma ve dönen ekipmanlar | X | X |  |  |  |  | X |  | X | X
Hoper / Silo /depolama ekipmanlar ve transferleri | X | X |  |  | X |  | X | X | X | X
Toz Toplama ve Hava-Toz Ayırştırma | X | X |  |  | X |  |  |  | X | X
Elektrikli ekipman sınıflandırılması |  |  | X | X |  |  |  |  |  | 

## Slide 38: Tehlikeli Bölge / ZONE Sınıfları (TOZ)
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 39: ZONE Sınıfı Örnekleri – Sprey Kurutucu
Ref VDI 2263 7.1
Jet Filtre
Sprey
Kurutucu
FBD
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 40: Aşırı Toz Birikimi – ZONE 22 Alanlar
ZONE 22 Çalışma Alanı Örnekleri
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 41: Alev Kaynakları- EN1127-1
EN1127-1 Alev Kaynakları Örnekleri
Elektrostatik alevlenme
Mekanik Kıvılcımlar
Sürtünme
Döner ekipmanda aşırı ısınma
Yabancı malzeme
Çarpma
Ekipmanda kırılma/bozulma
Sıcak iş izinleri
Toprak eksikliği
Ortama uygun olmayan elektrikli ekipman
Egzotermik reaksiyon
İçten yanma
Vs....
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 42: Alev Kaynakları- EN1127-1
ALEV KAYNAKLARI FORMU |  |  |  | 
PROSES ADI: | Toz MIE, mJ | Toz AIT , oC | Tarih: | Dolduran:
OLASI KAYNAKLAR (EN1127) |  |  | ALAKALI (EVET/HAYIR) | TOZU ALEVLENDİRME OLASILIĞI (sebepleri ile)
Sıcak Yüzeyler |  |  |  | 
Atev ve sıcak gazlar (sıcak parçacıklarıda dahil et) |  |  |  | 
Mekanik oluşan kıvılcım kaynakları |  |  |  | 
Elektrkli Ekipman |  |  |  | 
Kontrolsüz Elektrik Akımları, katodik korozyon koruması |  |  |  | 
Statik Elektrik |  |  |  | 
Korona Boşalımı |  |  |  | 
Brush Boşalımı |  |  |  | 
İlerleyen Brush Boşalımı |  |  |  | 
Cone Boşalımı |  |  |  | 
Kıvılcım Boşalımı |  |  |  | 
Yıldırım |  |  |  | 
Radyo Frekansı 10^4 Hz - 3x10^11 Hz |  |  |  | 
Elekktromanyetik Dalgalar 3x10^11-10^15 Hz arasi |  |  |  | 
Iyonlaşma Radyasyonu |  |  |  | 
Ultrasonik kaynaklar |  |  |  | 
Adiyabatik Sıkışma ve Şok Dalgası |  |  |  | 
Ekzotermik Reaksyon ve tozun kendinden yanması |  |  |  | 
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 43: Alev Kaynakları

## Slide 44: Yabancı Malzemeler
Kırılmış değrimen/shredder bıçakları
Kopmuş konveyör parçası

## Slide 45: Kıvılcım - Elektrosatik Boşalım
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 46: Alev Kaynakları
Chart: Toz Patlamaları Alev Kaynakları Dağılımı
| Sürtünme | Kıvılcım | Kimyasal reaktivite | Sıcak İş | Alev-kazan | Elektrik | Statik Elektrik | Aşırı ısınma | Sıcak yüzeyler | Bilinmiyenler
Sürtünme Kıvılcım Kimyasal reaktivite Sıcak İş Alev-kazan Elektrik Statik Elektrik Aşırı ısınma Sıcak yüzeyler Bilinmiyenler | 50 | 38 | 16 | 13 | 10 | 6 | 6 | 4 | 2 | 21
Ref: AICHE Center for Chemical Process Safety
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 47: Proses Ekipmanlarında Olası Alev Kaynakları
Ref: AICHE Center for Chemical Process Safety
 | Silo | Toz Toplayıcılar | Siklonlar | Mikser/Blender/Reaktör | Elek/Havalı Ayrıştırıcı | Konveyörler, elevatörler | Transfer Şutları | Değirmen/Öğütücü | Kurutucular/Kazanlar
Sürtünme |  |  |  | x | x | x |  | x | 
Kıvılcım | x | x |  | x | x | x |  | x | x
Kimyasal reaktivite |  |  |  | x |  |  |  |  | x
Sıcak İş | x | x | x | x | x | x | x | x | x
Kontrolsüz yakma |  |  |  |  |  |  |  |  | x
Elektrik | x | x | x | x |  | x | x | x | x
Statik Elektrik | x | x |  | x | x | x | x |  | 
Aşırı ısınma |  |  |  | x |  | x |  | x | x
Sıcak yüzeyler |  |  |  | x |  |  |  | x | x
Çarpma/yabancı cisim | x | x | x | x | x | x | x | x | 
İçten yanma | x |  |  |  |  |  |  |  | x
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 48: Toz Patlama Risklerini Nasıl Azaltabiliriz ?
Patlama Engelleyici Önlemler
Topraklama, Bond
Kıvılcım Algılama ve Söndürme
Dönen ekipmanlarda aşırı ısı algılama
Devir bekçisi kullanımı
Tozsuzlaştırma
Ortam Temizliği, vs
Patlama Korunma Önlemleri
İnerting sistemleri
Patlama basıncına dayanımlı ekipmanlar ve hatlar
Patlama tahliye kapakları
Patlama söndürme sistemleri
VE Patlama izolasyonu (patlama yayılma engelleme)
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 49: Patlama Korunma
  Explosion Suppression /
  Patlama Sönümleme
  Explosion Isolation /
  Patlama İzolasyonu
  Explosion Vents /
  Patlama Kapakları
  Engineering Services /
  Mühendislik Hizmetleri
Design /
Sistem Tasarımı
Maintenance
Bakım Hizmeti
Material Testing
Malzeme Testleri

## Slide 50: Patlama Engelleme
  Spark Detection & extinguishment /
  Kıvılcım Algılama ve Söndürme
  Flame Detection/
  Alev Algılama
  CO and Smoke Detection /
  Karbon Monoksit ve Duman Algılama
  Overheat Detection /
  Makina Aşırı Isınma Algılama

## Slide 51: Elektrosatik Kontroller
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 52: Kıvılcım Algılama ve Sönümleme
Hassas Algılama
300oC Altı Isıda sıcak parçacık algılama
Rulman, blower,
Dönen ekipman aşırı ısınma algılama
Atomize su kıvılcım söndürme
Kıvılcım/sıcak parçacık algılama,geniş spektrum, geniş açı
Kontrol paneli

## Slide 53: Kıvılcım Algılama ve Sönümleme

## Slide 54: IEP Uygulamalar – Filtreler

## Slide 55: Uygulamalar - Tozsuzlaştırma

## Slide 56: Uygulamalar – Pelet Presleri

## Slide 57: Uygulamalar – Silo ve Bunkerler

## Slide 58: Patlama Korunma Sistemi Seçimi
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 59: Patlama Tahliye
Standart patlama kapağı ve
patlama izolasyonu
Alevsiz patlama kapağı ve
patlama izolasyonu
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 60: Patlama Tahliye / Vent
TS EN 14797:2006 Patlama Tahliye Tertibatları (Explosion Venting Devices)
  Fonkisyon ve mekanik bütünlük testleri
  Verimlilik testleri
  Statik açılma basıncı testleri
  Sıcaklık etkisi testleri
  Spesifik ağırık etkisi testleri
  Etiketleme standartları (Bölüm 10.3.2)
    Üretici ad ve adresi
    CE İşareti (İlgili standardına uygun ebatlarda)
    EX işareti (İlgili standardına uygun ebatlarda)
    Gerekli uyarılar (basmayınız vs.)
    Uygulanan Standart
    Model ve statik açılma basıncı bilgileri
Üretici firmanın da ATEX üretici onayı olmalı

## Slide 61: Patlama Tahliye / Patlama Kapakları
Basit ve hesaplı uygulama
Ekipman üzerin yerleştirilen zayıf membran ~ 0.1bar açılma
Sadece basıncı tahliye eder– Alevi yok etmez
Patlama sonrası yangın oluşabilir
Etrafında güvenli alan olmalı- alevsizler dahil
Tahliye kapağı açıklığından alev topu çıkışı ~ 8 x V
Basınç
Zaman
Pmax
Patlama kapağı yok
Ekipman dayanımı
P red – İndirgenmiş basınç
Pstat –Kapak açılış basıncı
Patlama kapağı var
Basınç-Zaman Grafiği

## Slide 62: Patlama Tahliye Kapakları
Alevsiz
Standart
IndoorVent IV
Yuvarlak Panel
IV8
Yüksek Verimli
GE  Domed, vakuma uygun
GE  Domed, vakuma uygun
KE  Düz, flanş gerekli
KER  Düz, flanş dahil
Patlama Kapakları
EVN 2.0
Uygulama Kolaylığı
Açılır-kapanır
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 63: Filtrelerde Patlama Kapak Kullanımı
2018 © IEP Technologies – izinsiz kopyalanmaz

## Slide 64: Elevatörlerde Patlama Kapağı Kullanımı

## Slide 65: Patlama Tahliye Kapakları - Elevatörler
NFPA 61
VDI 2263

## Slide 66: Silolarda Patlama Kapağı Kullanımı

## Slide 67: Alevsiz Patlama Kapağı
EVN Alevsiz Patlama Kapağı (Çok Kullanımlı Tasarım)

## Slide 68: IV8 Alevsiz Patlama Kapağı

## Slide 69: Alevsiz Patlama Kapakları -VDI 2263 8.1

## Slide 70: 100% Pasif Korunma Çözümü
Toz Emiş Hattı üzerinde Flap
Temiz hava çıkış hattı üzeri Ventex
EVN Alevsiz Patlama Kapağı

## Slide 71: Patlama Söndürme
Aktif sistem
Kapalı alanlar
Veya tahliye kapakları kullanılmamadığı zamanlar
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 72: Patlama Söndürme
Ref – GMP proses, filtre patlama korunması
Notes: Explosion protection addresses both the vessel and the interconnection to other plant items:
Starting with vessel protection, there are three main means. First we have containment whereby the plant is made very strong such that it can withstand the maximum pressure generated by an unmitigated explosion event ~10 bar. This is an expensive option and in the case of large vessels is not pratical.
Explosion suppression, where the majority of our business lies, relies on early detection of an explosion and then the rapid deployment of suppressant, such that the explosion pressure is reduced below the strength of the plant.
Finally we have explosion venting, which is effectively a weak panel in the vessel which yields at low pressure allowing the release of product and flame. The photo shows efficacious deployment of venting to protect a bag filter, but as you can see results in a very large fireball being ejected from the vessel. This fireball obviously causes a risk to personnel and the possibility of post explosion fires and consequent explosion occurrences in other plant.
The solution here in the case for venting and suppression determines the hardware count and the reduced explosion pressure, Pred.
These techniques are well understood and have been deployed in the field for over 30 years.

## Slide 73: Dinamik Patlama Basıncı Algılama

## Slide 74: Örnek: Kurutucular

## Slide 75: Örnek: Kurutucular

## Slide 76: Örnek: Değirmenler/Transfer Hatları

## Slide 77: Patlama İzolasyonu
İhtiva, patlama kapakları veya söndürme uygulamalarının tamamı izolasyon sistemleri ile tamamlanır
Bağlantılı ekipmanlar arası alev geçişi patlama etkisini arttırır– Flame Jet Ignition (İSG 6331 Madde 5)
REF: NFPA 68-98 Bölüm 3-6.7 ve VDI 2263 Bölüm 4, NFPA 654-97 Bölüm 3-1.2

## Slide 78: Patlama İzolasyonu
Pasif İzolasyon
(ör. Detektör veya kontrol sistemi ihtiyacı yok)
  Aktif İzolasyon
  (ör. HRD söndürme tüpleri, hızlı slide vanalar)
IsoFlap

## Slide 79: Patlama İzolasyonu

## Slide 80: Patlama İzolasyonu
Mekanik İzolasyon - Flap Vana
Aktif Kimyasal İzolasyon
Aktif Mekanik İzolasyon
Slide Vana

## Slide 81: Patlama Korunma Olmadığı Zaman

## Slide 82
Teşekkürler, Emre Ergun
Emre.Ergun@Hoerbiger.com
0533-457-4412

## Slide 83
EKLER

## Slide 84: Kanunlar ve Standartlar
Çalışanların Patlayıcı Ortamların Tehlikelerinden Korunması Hakkında Yönetmelik (ISG 6331)
Resmi Gazete 28633 (6331 Numaralı İSG Kanunu Madde 5)
(1) İşveren, patlamaların önlenmesi ve bunlardan korunmayı sağlamak amacıyla, yapılan işlemlerin doğasına uygun olan teknik ve organizasyona yönelik önlemleri alır. Bu önlemler alınırken aşağıda belirtilen temel ilkelere ve verilen öncelik sırasına uyulur;
a) Patlayıcı ortam oluşmasını önlemek,
b) Yapılan işlemlerin doğası gereği patlayıcı ortam oluşmasının önlenmesi mümkün değilse patlayıcı ortamın tutuşmasını önlemek,
c) Çalışanların sağlık ve güvenliklerini sağlayacak şekilde patlamanın zararlı etkilerini azaltacak önlemleri almak.
(2) Birinci fıkrada belirtilen önlemler, gerektiğinde patlamanın yayılmasını önleyecek tedbirlerle birlikte alınır. Alınan bu tedbirler düzenli aralıklarla ve işyerindeki önemli değişikliklerden sonra yeniden gözden geçirilir.

## Slide 85: DIN/EN Standardları
TS/EN 60079-10-1Patlayıcı ortamlar- Bölüm 10-1: Alanların sınıflandırılması - Patlayıcı gaz ortamları
TS/EN 60079-10-2 Patlayıcı ortamlar- Bölüm 10-2: Tehlikeli bölgelerin sınıflandırılması-Yanıcı toz atmosferler
DIN EN 1127-1 Explosive atmospheres, explosion protection Part 1: Fundamental principles and methods
DIN EN 60079 Installation of electrical equipment in hazardous areas, Repair and maintenance of operators intended for use in hazardous areas
VDI 2263 Dust fires and dust explosions Hazards – Assessment – Protection measures
DIRECTIVE 1999/92/EC OF THE EUROPEAN PARLIAMENT AND OF THE COUNCIL of 16 December 1999 on minimum requirements for improving the safety and health protection of workers potentially at risk from explosive atmospheres (15th individual Directive within the meaning of Article 16(1) of Directive 89/391/EEC)

## Slide 86: VDI Standardları

## Slide 87: NFPA Standardları
  NFPA 652 Yanıcı/Parlayıcı Tozlar ve Toz Tehlike Analizleri
  NFPA 654 Yanabilir/patlayabilir tozlar ve parçacıkları işleyen tesisler
  NFPA 664 Odun işleyen prosesler
  NFPA 61 Gıda ve Tahıl Tozları işleyen prosesler
  NFPA 484 Metal tozları
  NFPA 30B Aerosol ürünleri
  NFPA 68 Patlama kapakları
  NFPA 69 Patlamaları Engelleyici Sistemler
  NFPA 85 Kazan ve Yakma Sistemleri (kömür)
(c) 2016 IEP Technologies A.S. - İzinsiz Kopyalanmaz
Notes: NFPA issues a number of national consensus standards that address the hazards of combustible dust. For example, NFPA 654, Standard for the Prevention of Fire and Dust Explosions from the Manufacturing, Processing, and Handling of Combustible Particulate Solids, addresses the hazards of combustible dust in a general manner. Specific industries are excluded from NFPA 654, but are covered by other NFPA standards, including NFPA 61, Standard for the Prevention of Fires and Dust Explosions in Agricultural and Food Processing Facilities; NFPA 484, Standard for Combustible Metals; NFPA 655, Standard for Prevention of Sulfur Fires and Explosions; and NFPA 664, Standard for the Prevention of Fires and Explosions in Wood Processing and Woodworking Facilities. These five NFPA combustible dust standards have mandatory secondary references to a large number of other standards. The 2006 edition of NFPA 654 mandates compliance with 36 other NFPA standards. These 36 secondary references, in turn, reference additional standards. In effect, no one standard comprehensively addresses the hazards of combustible dust, which may pose difficulties for some employers trying to develop programs to mitigate combustible dust hazards. In addition, the provisions of these five NFPA standards differ, which may add to these difficulties. Some elements of protection are addressed in some standards but not in others; other elements are addressed in different ways in the various standards. For example, NFPA 61, 484, and 654 contain provisions for drive belts, while NFPA 655 and 664 have no provisions directly addressing drive belts. In addition to the NFPA standards listed above, NFPA issues a number of standards that cover the design and installation of protection systems specific to deflagration and explosion hazards, including combustible dust. Two of these standards are NFPA 68, Standard on Explosions Protection by Deflagration Venting, and NFPA 69, Standard on Explosion Prevention Systems

## Slide 88: FM Datasheets
Notes: NFPA issues a number of national consensus standards that address the hazards of combustible dust. For example, NFPA 654, Standard for the Prevention of Fire and Dust Explosions from the Manufacturing, Processing, and Handling of Combustible Particulate Solids, addresses the hazards of combustible dust in a general manner. Specific industries are excluded from NFPA 654, but are covered by other NFPA standards, including NFPA 61, Standard for the Prevention of Fires and Dust Explosions in Agricultural and Food Processing Facilities; NFPA 484, Standard for Combustible Metals; NFPA 655, Standard for Prevention of Sulfur Fires and Explosions; and NFPA 664, Standard for the Prevention of Fires and Explosions in Wood Processing and Woodworking Facilities. These five NFPA combustible dust standards have mandatory secondary references to a large number of other standards. The 2006 edition of NFPA 654 mandates compliance with 36 other NFPA standards. These 36 secondary references, in turn, reference additional standards. In effect, no one standard comprehensively addresses the hazards of combustible dust, which may pose difficulties for some employers trying to develop programs to mitigate combustible dust hazards. In addition, the provisions of these five NFPA standards differ, which may add to these difficulties. Some elements of protection are addressed in some standards but not in others; other elements are addressed in different ways in the various standards. For example, NFPA 61, 484, and 654 contain provisions for drive belts, while NFPA 655 and 664 have no provisions directly addressing drive belts. In addition to the NFPA standards listed above, NFPA issues a number of standards that cover the design and installation of protection systems specific to deflagration and explosion hazards, including combustible dust. Two of these standards are NFPA 68, Standard on Explosions Protection by Deflagration Venting, and NFPA 69, Standard on Explosion Prevention Systems